## Slide 1
PERFBOARD BUILD GUIDE
Multiple-IMU Wearable Sensor System
XIAO ESP32C3 + BNO085 + LiPo 3.7V
1 Master · 2 Slaves · Two-Sided Perfboard
Joonho · Hanyang University · 2026

## Slide 2
BILL OF MATERIALS
Per node — build 3 identical boards (1 master + 2 slaves)
COMPONENT | SPEC | ×1 | ×3 | NOTES
XIAO ESP32C3 | Seeed Studio | 1 | 3 | Built-in LiPo charger via USB-C
BNO085 Breakout | Adafruit, I2C 0x4A | 1 | 3 | Has onboard 10kΩ pull-ups
LiPo Pouch Cell | 3.7V, 400–1000mAh | 1 | 3 | JST-PH 2-pin, with protection circuit
SPST Slide Switch | ≥0.3A rated | 1 | 3 | Mounted on housing (not on perfboard)
TP4057 Charger | USB-C, 1A, 3.7V | — | 1 | Separate charging station (not on board)
Perfboard | 5×7cm, double-sided | 1 | 3 | Two-sided for ground plane
Female Pin Headers | 1×7 (XIAO), 1×9 (BNO) | 3 | 9 | Socket mount — removable for flashing
100nF Ceramic Cap | 0.1µF, ≥10V | 1 | 3 | Decoupling near BNO085 VIN
Hookup Wire | 22–26 AWG solid | — | — | ~5 connections per board

## Slide 3
PERFBOARD — TOP SIDE
Compact wearable layout (~3.3 × 2.5 cm) · BNO085 overhangs right edge
Compact Board
(13×10 holes)
XIAO
ESP32C3
USB-C
D0
D1
D2
D3
D4 (SDA)
D5 (SCL)
D6
5V
GND
3V3
D10
D9
D8
D7
BAT+ BAT−
BNO085
(overhangs)
pins on
board
VIN
3Vo
GND
SCL
SDA
INT
100nF
SDA (top, L)
SCL (bottom, L)
3V3→VIN
GND (bottom)
wires off-board →
switch on housing
COMPACT LAYOUT
WIRE ROUTING
3V3 → VIN
solid (top side)
GND
L-shape (bottom side)
SDA (GPIO6)
L-shape, TOP (10 holes)
SCL (GPIO7)
L-shape, BOTTOM (10 holes)
Battery (BAT±)
off-board to switch
KEY CONNECTIONS
3V3 → BNO085 VIN (top)
GND → BNO085 GND (bottom)
D4 (GPIO6) → SDA (top, L-shape, cross at gap)
D5 (GPIO7) → SCL (bottom, L-shape, cross at gap)
BAT± → external switch → LiPo
100nF cap near BNO085 VIN

## Slide 4
PERFBOARD — BOTTOM SIDE
Solder traces and wiring (compact board, viewed from below — mirrored)
BOTTOM VIEW
(compact, mirrored)
XIAO
(ghost)
BNO085
(ghost)
SCL (solid, L)
SDA (ghost, top)
GND L-route (solid)
3V3 (ghost)
BAT+ BAT−
to housing
switch
SOLDERING TIPS (COMPACT)
Board cutting
Cut perfboard to 13×10 holes (~3.3 × 2.5 cm). File edges smooth to prevent wire snags.
BNO085 overhang
Only pin header sits on board; body overhangs right edge. Use dashed box in top-view diagram to show extent.
Bottom GND plane
Use continuous bottom-side copper for GND bus. Route as L-shape: vertical from XIAO down, then horizontal to BNO085 GND.
I2C crossing
BNO085 pin order (SCL before SDA) requires crossing. SDA on top side, SCL on bottom — they cross at gap col on opposite sides.
Battery off-board
BAT± wires leave board toward external switch on housing. Hot-glue wires for strain relief.
Tight spacing
Only 1 gap column between XIAO right pins and BNO085 pin header. Route 3V3 through this gap on top side.

## Slide 5
BATTERY WIRING
LiPo connection with external switch on housing · TP4057 separate charging station
LiPo 3.7V
400–1000mAh
SWITCH
(on housing)
XIAO ESP32C3
BAT+ / BAT− pads
(+)
BAT+
(−)
BAT−
Charging: TP4057 Station
Use a separate TP4057 USB-C module (1A) as a charging station. Disconnect from board to charge. XIAO has a built-in charge IC (~50mA) but it's too slow. Never connect both chargers simultaneously.
LiPo Safety
Use cells with built-in protection circuit. Verify polarity before connecting. Reversed polarity will damage the XIAO.
Battery Life Estimate
Parameter | Value
XIAO active (WiFi TX) | ~80–120mA
BNO085 active | ~15mA
Total (streaming) | ~95–135mA
500mAh → runtime | ~3.5–5 hrs
1000mAh → runtime | ~7–10 hrs

## Slide 6
TESTING CHECKLIST
BEFORE applying power — multimeter checks
1 Visual Inspection
All solder joints shiny and concave (no cold joints)
No solder bridges between adjacent pads
Pin headers seated flush and straight
Battery wires have strain relief (hot glue)
2 Continuity Tests (Ω mode)
3V3 (XIAO) → VIN (BNO085): should beep / 0Ω
GND (XIAO) → GND (BNO085): should beep / 0Ω
D4/GPIO6 → SDA (BNO085): should beep / 0Ω
D5/GPIO7 → SCL (BNO085): should beep / 0Ω
BAT+ pad → external switch wire: should beep / 0Ω
BAT− pad → LiPo (−) wire: should beep / 0Ω
3 Short-Circuit Test (Ω mode)
3V3 ↔ GND: must NOT beep (should show >1kΩ)
SDA ↔ SCL: must NOT beep
BAT+ ↔ BAT−: must NOT beep
5V ↔ GND: must NOT beep

## Slide 7
TESTING CHECKLIST
AFTER applying power — voltage and function checks
4 Voltage Measurements (V DC mode)
LiPo voltage: 3.5–4.2V (below 3.5V = charge first)
External switch ON → XIAO 3V3 pin: should read 3.3V (±0.1V)
BNO085 VIN: should match XIAO 3V3 (~3.3V)
XIAO 5V pin (USB powered): should read ~5V
No excessive heat on any component after 30 seconds
5 USB Serial Test (one node at a time)
Plug USB-C → PC should enumerate serial port
idf.py monitor shows boot log, no crash loops
Slave: beacon sending confirmed in serial log
Master: 'serial_cmd_task started' in log
6 I2C / BNO085 Verification
I2C scan shows device at 0x4A
BNO085 reports rotation vector data (no NaN, no zeros)
Quaternion values change when board is rotated
All 3 reports active (rotation + accel + gyro)
7 Battery-Only Operation
Unplug USB-C. External switch ON → XIAO powers from LiPo
XIAO 3V3 pin still reads 3.3V on battery
Slave sends beacons on battery power
External switch OFF → all power cut (0V on 3V3)

## Slide 8
TROUBLESHOOTING
XIAO won't power on from battery
→
Check external switch continuity and wire connections. Verify LiPo has charge (>3.5V). Check BAT+ and BAT− pad solder joints — they're small and easy to get cold joints on.
BNO085 not detected (I2C scan empty)
→
Check 3V3→VIN and GND→GND continuity. Verify BNO085 is properly seated in headers. Check for solder bridges between SDA/SCL.
I2C data corrupted / intermittent
→
Add 100nF decoupling cap closer to BNO085. Shorten I2C wires. Check for cold solder joints on SDA/SCL.
XIAO resets randomly on battery
→
LiPo voltage too low (replace/charge). Add 10µF electrolytic cap across BAT±. Check for loose connections causing brownout.
USB-C won't enumerate
→
Remove XIAO from socket, test standalone. Check no short between 5V and GND. Try different USB cable (data-capable, not charge-only).
ESP-NOW packets not received
→
Verify both boards flashed with correct firmware (master vs slave). Check WiFi antenna area is not blocked by ground plane copper on perfboard.